## Slide 1
Microprocessor & Computer Architecture (μpCA)
UE22CS252B
Session - 2.4

## Slide 2
Microprocessor & Computer Architecture (μpCA)
UE22CS252B
Pipeline Processor: Data Hazard 1

## Slide 3
  Suppose initially, register i holds the number 2i
  (ie. R3 = 6; R6=12; R8 = 16…)
  What happens when the following sequence is executed in 5-stage pipeline?
add R3, R10, R11
ldr R8, [R3, #50]
sub R11, R8, R7
- this should add 20 + 22, putting result 42 into r3
- this should load r8 from memory location 42+50 = 92
- this should subtract 14 from that just-loaded value from Mem[92]
Consider a Scenario
Data Hazards

## Slide 4
Cycle 1

## Slide 5
Cycle 2

## Slide 6
Cycle 3

## Slide 7
Cycle 4

## Slide 8
EXAMPLE
Consider the following sequence:
sub R2, R1, R3 and R12, R2, R5 orr R10, R6, R2 add R4, R2, R2 str R5, [R2, #100]
DEPTH OF HAZARD = 3 cycles
IF ID EX MEM WB
IF ID EX MEM WB
IF ID EX MEM WB
IF ID EX MEM
IF ID EX

## Slide 9
Data Dependency
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
ID
EXE
MEM
IF
WB
ID
EXE
MEM
IF
WB
ID
EXE
MEM
IF
WB
ID
EXE
MEM
IF
WB
ID
EXE
MEM
IF
WB

## Slide 10
Data Dependencies
Three types of data dependencies defined in terms of how succeeding instruction depends on preceding instruction
  RAW: Read after Write or Flow dependency
  (True Dependency)
  WAR: Write after Read or anti-dependency
  (Anti Dependency)
  WAW: Write after Write
  (Output Dependency)

## Slide 11
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3
Data Dependencies

## Slide 12
Example program (a) with two instructions
  i1: load r1, a;
  i2: add r2, r1,r1;
Program (b) with two instructions
  i1: mul r1, r4, r5;
  i2: add r2, r1, r1;
Both cases we cannot read in i2 until i1 has completed writing the result
  In (a) this is due to load-use dependency
  In (b) this is due to define-use dependency
Data Dependencies

## Slide 13
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen if in pipeline:-
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7
Data Dependencies

## Slide 14
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen if in pipeline:
All instructions take 5 stages, and Writes are always in stage 5
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7
If Executed Out of order by the Compiler, may lead to wrong results
Data Dependencies

## Slide 15
Example program (a):
  i1: mul r1, r2, r3;
  i2: add r2, r4, r5;
Example program (b):
  i1: mul r1, r2, r3;
  i2: add r1, r4, r5;
both cases we have dependence between i1 and i2
  in (a) due to r2 must be read before it is written into
  in (b) due to r1 must be written by i2 after it has been written into by i1
WAR and WAW Dependency

## Slide 16
Problem:
  i1: mul r1, r2, r3;
  i2: add r2, r4, r5;
Is this really a dependence/hazard ?
WAR and WAW Dependency

## Slide 17
Solution: Rename Registers
  i1: mul r1, r2, r3;
  i2: add r6, r4, r5;
Register renaming can solve many of these false dependencies
  note the role that the compiler plays in this
  specifically, the register allocation process--i.e., the process that assigns registers to variables
WAR and WAW Dependency

## Slide 18
Consider the following sequence:
sub R2, R1, R3 and R12, R2, R5 orr R10, R6, R2 add R4, R2, R2 str R5, [R2, #100]
DEPTH OF HAZARD = 3 cycles
IF ID EX MEM WB
IF ID EX MEM WB
IF ID EX MEM WB
IF ID EX MEM
IF ID EX
EXAMPLE

## Slide 19
THANK YOU
Team MPCA
Department of Computer Science and Engineering